## Slide 1
Network Intrusion Detection
with Machine Learning
John MacIntyre · Jacob Marshall
Mentors: Dr. Namsong Wu · Dr. Gurman Gill · CS 470

## Slide 2
The Problem
2
Network attacks are growing in frequency and sophistication, but most ML-based IDS models prioritise accuracy over deployability.
What is an IDS?
An Intrusion Detection System monitors network traffic and classifies flows as normal or one of several attack types in real time.
The Gap in Published Research
Most IDS papers report high accuracy but never measure model size, latency, or memory footprint, the metrics that determine if a model can actually be deployed.
Why Size Matters
Real deployments run on embedded monitors, IoT gateways, and vehicle-level hardware. A 67 MB Random Forest is not feasible on a device with 1 GB RAM and strict latency requirements.
Our Goal
Can feature reduction produce a model under 1 MB that retains high detection accuracy? We benchmark three compact models against two published reference studies.

## Slide 3
Research Question & Objectives
3
Research Question: Which intrusion detection model provides the best balance between detection performance and computational efficiency for practical deployment?
1. Compare ML models for IDS performance
Decision Tree, XGBoost, LightGBM trained on the same features and evaluated identically
2. Measure computational efficiency
Model size (KB), inference latency (ms), throughput (samples/sec), memory footprint
3. Apply feature reduction
Reduce 79 raw features to a compact set using statistical and model-based ranking
4. Benchmark against published work
Compare our results to two reference notebooks using the same CICIDS2017 dataset

## Slide 4
Three-Phase Pipeline
4
Dataset: CICIDS2017, 2.83M labelled network flows, 79 features, 15 attack classes
01
Data Cleaning
▸ Remove inf / NaN / duplicates
▸ Drop zero-variance & identical columns
▸ Memory downcast (44% reduction)
▸ Result: 2,499,641 clean rows, 66 cols
→
02
Feature Engineering
▸ Group 15 labels → 7 classes
▸ Correlation filter (r > 0.95)
▸ Kruskal-Wallis + RF importance
▸ Result: 10 final features selected
→
03
Model Training
▸ Decision Tree (depth sweep)
▸ XGBoost (Optuna 50 trials, GPU)
▸ LightGBM (Optuna 15 trials)
▸ Benchmark: size, latency, F1, throughput

## Slide 5
Data Cleaning
5
01
Infinite values → median imputation
Flow Bytes/s and Packets/s contained 4,376 infinite values. Replaced with column median, recovering rows that dropna() would discard.
02
Negative flow duration removed
115 rows had negative Flow Duration (physically impossible). Removed as instrumentation errors.
03
Zero-variance & identical columns dropped
8 constant columns dropped (e.g. Bwd PSH Flags). 5 byte-for-byte duplicate columns removed using Series.equals(). Found SYN Flag Count = Fwd PSH Flags
04
Duplicates removed + memory downcast
308,373 duplicate rows removed. float64→float32 downcast achieved 44% memory reduction (1,400→780 MB). Post-downcast dedup removed 22,614 precision-collision rows.
Final: 2,499,641 rows · 780 MB (−44%)

## Slide 6
How We Selected 10 Features
6
79 raw features
Original CICIDS2017 columns
▼
48 features
Removed 31 correlated pairs (r > 0.95)
▼
10 features selected
Combined Kruskal-Wallis + RF importance ranking
Why two methods?
Kruskal-Wallis Statistical test, how much does each feature's distribution differ across attack classes? RF Importance How often does each feature appear in tree splits? Features used near the root score highest. Combined score Normalise both 0–1 and average. Select top 10 where both agree.

## Slide 7
10 Features Retained Most of the Predictive Power
7
5 → 10 features
+0.058 F1
10 → 30 features
+0.014 F1
Model size at 10
27 KB

## Slide 8
Per-Class F1 — All Three Models
8
Key takeaways
✓ DDoS, Normal, Port Scanning, Brute Force — all models 0.95+ F1
↑ XGBoost and LightGBM significantly improve Bot and Web Attack over DT
! Bot (0.51–0.61) and Web Attack (0.00–0.65) are the hardest classes, a feature space problem, not a model failure

## Slide 9
Full Benchmark — All Models
9
▸ DT is 2,440× smaller than Ref1 RF
▸ Our XGB is 8% smaller than Ref1 XGB with 23× higher throughput
▸ KNN (Ref1) terminated after 60+ min — infeasible at scale

## Slide 10
Confusion Matrices — All Three Models
10
Read the diagonal: bright values = correct predictions. Off-diagonal = misclassifications. Bot row shows most missed predictions (low recall) across all three models.

## Slide 11
Random Forest - accuracy/size
11

## Slide 12: Random Forest benchmarks
index | Model | Trees | Max Depth | Accuracy | Precision | Recall | F1 | KB | ms/sample | Throughput/s
0 | RF 1 (100 trees, d=) | 100 | None | 0.9959 | 0.9962 | 0.9959 | 0.996 | 146515 | 0.003887 | 257277
1 | RF 2 (75 trees, d=20) | 75 | 20 | 0.9868 | 0.9961 | 0.9868 | 0.991 | 47920 | 0.002823 | 354205
2 | RF 3 (50 trees, d=16) | 50 | 16 | 0.9801 | 0.9952 | 0.9801 | 0.9871 | 18727 | 0.001974 | 506675
3 | RF 4 (40 trees, d=14) | 40 | 14 | 0.9761 | 0.9934 | 0.9761 | 0.9841 | 10442 | 0.001532 | 652809
4 | RF 5 (30 trees, d=12) | 30 | 12 | 0.9669 | 0.9938 | 0.9669 | 0.9795 | 5274 | 0.001256 | 796103
5 | RF 6 (25 trees, d=10) | 25 | 10 | 0.9488 | 0.9899 | 0.9488 | 0.968 | 2256 | 0.001067 | 937317
6 | RF 7 (20 trees, d=8) | 20 | 8 | 0.8592 | 0.9723 | 0.8592 | 0.9088 | 777 | 0.00092 | 1087383
7 | RF 8 (15 trees, d=7) | 15 | 7 | 0.7356 | 0.9561 | 0.7356 | 0.8195 | 383 | 0.00079 | 1265062
8 | RF 9 (10 trees, d=6) | 10 | 6 | 0.6299 | 0.9544 | 0.6299 | 0.7374 | 145 | 0.000669 | 1494308
9 | RF 10 (5 trees, d=5) | 5 | 5 | 0.476 | 0.9076 | 0.476 | 0.5873 | 43 | 0.000459 | 2176306
10 | RF 11 (4 trees, d=4) | 4 | 4 | 0.0878 | 0.9546 | 0.0878 | 0.0918 | 22 | 0.000442 | 2263908
11 | RF 12 (3 trees, d=3) | 3 | 3 | 0.0628 | 0.9444 | 0.0628 | 0.0688 | 12 | 0.000403 | 2478757
12 | RF 13 (2 trees, d=3) | 2 | 3 | 0.0562 | 0.9054 | 0.0562 | 0.0604 | 8 | 0.000364 | 2747201
13 | RF 14 (1 trees, d=2) | 1 | 2 | 0.0002 | 0.799 | 0.0002 | 0.0005 | 4 | 0.000308 | 3242647

## Slide 13
12
An Unexpected Finding
Adding more features to the Decision Tree made it smaller
Feature Count
Model Size
F1 Weighted
10 features
27.4 KB
0.9896
15 features
25.2 KB
0.9903
20 features
23.4 KB
0.9911
30 features
22.9 KB
0.9931
Why?
More discriminative features let the tree reach pure leaf nodes earlier, fewer total splits needed = smaller file size.
The throughput tradeoff: 10 feat = 12,679K/s → 30 feat = 5,810K/s. Still 3× faster than XGBoost at 1,956K/s.

## Slide 14
Key Findings
13
27 KB is viable
A Decision Tree at depth=8 with 10 features achieves 98.96% weighted F1, 0.76 ms latency, and 12.6M samples/sec throughput, under 30 KB on disk.
Gradient boosting matches references at fraction of the size
LightGBM (834 KB) and XGBoost (1,007 KB) match Ref1's accuracy while being up to 80× smaller than their Random Forest (67 MB).
More features = smaller DT
Adding targeted features reduced model size (27→22 KB) because the tree solves minority classes earlier and terminates branches sooner.
Bot and Web Attack remain hard
F1 of 0.51–0.65 across all models. Timing-based features cannot fully separate these classes, backward packet and TCP handshake features are needed.